## Slide 1
Maximum Synergy Under One Roof

## Slide 2
How to Improve Renewable Energy Storage with MQTT, Modbus, and InfluxDB Cloud Dedicated
Ricardo Kissinger | München, 26.09.2023

## Slide 3: Agenda – Introduction to Company
01
Introduction of ju:niz Energy GmbH
Who we are and what we do
02
Showcase of Generation 1.0 BESS
References from our first Generation BESS
03
Showcase of Generation 1.5 BESS
A few examples from our current “SMAREG“ projects

## Slide 4: Introduction of ju:niz Energy GmbH
01

## Slide 5: ju:niz Energy
Founded
2014
Employees2023
66
Installed Capacity
145 MWh
Core business
Intelligent large-scale storage systems that are operated in a grid-serving and economical manner.
Decentral energy supply of renewable energies, battery storage and hydrogen for district areas
intelligent energy management systems that control both the battery storage systems and the decentral energy system for optimal use.

## Slide 6: Our projects within Germany
Juwi 1 Schmölln | 2,9 MW/ 3 MWh
Siemens Fluence Wölkisch | 4,8 MW/ 5,2 MWh
Frankfurt Energy Großenh. | 1,5 MW/ 1,6 MWh
SMAREG 9 Freiberg |24 MW/ 24 MWh
SMAREG 3 Eisfeld | 12 MW/ 12 MWh
SMAREG 4 Wartburgspeicher Eisenach | 60 MW/ 67 MWh
SMAREG 5 Hildburghausen | 12 MW/ 13,6 MWh
Speicher Petersaurach | 1,1 MW/ 1,4 MWh
Speicher Freyung | 0,6 MW/ 1,2 MWh
SP Garching | 1,4 MW/ 1,2 MWh
Greenrock Trostberg | 1,2 MW/ 1,5 MWh
In Betrieb
Im Bau
SMAREG 8 Calbe | 24 MW/ 24 MWh
Speicher Echte | 1,1 MW/ 1,4 MWh
SMAREG 2 Breitenworbis | 10 MW/ 11 MWh
Smartbooster Gotha | 11 MW/ 11 MWh
Speicher Heuchelheim | 4,2 MW/ 4,2 MWh
Speicher Kempten | 16,0 MW/ 8,5 MWh
Speicher Leinburg | 1,0 MW/ 1,4 MWh
Juwi 2 Seckach | 3,6 MW/ 3,7 MWh
SMAREG 6 Gunzenhausen | 24 MW/ 24 MWh
SMAREG 7 Monheim | 12 MW/ 12 MWh
LEW Rain am Lech | 1,5 MW/ 1,6 MWh
BayWa München | 0,2 MW/ 0,2 MWh
SMAREG Energieversorger Leinau | 8,7 MW/ 3,7 MWh
Fuchstal | 5,8 MW/ 3,4 MWh

## Slide 7: Showcase of Generation 1.0 BESS
02

## Slide 8: Introduction to Generation 1.0 BESS
Generation 1.0 BESS
  25 Energy Storage plants across Germany
    Starting capacity 150kwh
    Average 1MWh capacity
    Up to 11MWh capacity
  Using mainly Samsung NMC Batteries and “Second Life” Batteries with LMO
Main Usage cases:
  Primary Frequency Control (Main Usage scenario)
  Peak Shaving
  Self-Supply for Electric Energy
  Reduction of Distribution Grid Fees

## Slide 9: Large-scale storage increases flexibility in the energy supply for industry/commerce and in the electricity grid
> 10 MWh
< 5 MWh
iEMS
Operational Services
Frequency reserve and trading
Peak Shaving, Optimisation of own comsumption, 7000h for industry and district areas

## Slide 10: PRL-Speicher Garching near by Munich
Customer | Forschungsprojekt
Location | Campus der Technischen Universität München
Completion | 2016
Power | 1,4 MW
Capacity | 1,2 MWh
System | Samsung SDI / Daimler
Design | 40 ft Battery container Rectifier Transformer
EMS | Smart Power iEMS
Technical Design
Key Facts

## Slide 11: JUWI Schmölln - First German Innovation project “Wind Energy and Energy Storage”
Customer | Juwi
Location | Schmölln
Completion | 2022
Power | 2,9 MW
Capacity | 3 MWh
System | SAMSUNG SDI
Design | 40 ft Battery container Rectifier
EMS | Smart Power iEMS
Technical Design
Key facts

## Slide 12: SMAREG 1 - Smartbooster
Customer | Investor project
Location | Gotha
Completion | 2020
Power | 11 MW
Capacity | 11 MWh
System | SAMSUNG SDI
Design | 40 ft Battery container Rectifier Transformer Transfer station
EMS | Smart Power iEMS
Technical Design
Key Facts

## Slide 13: VWEW Leinau
Customer | Industrial Customer
Location | Kaufbeuren
Completion | 2021
Power | 7,3 MW
Capacity | 3,7 MWh
System | SAMSUNG SDI
Design | 20ft Battery container Rectifier Transformer
EMS | Smart Power iEMS
Technical Design
Key Facts

## Slide 14: Showcase of Generation 1.5 BESS
03

## Slide 15: Introduction to Generation 1.5 BESS
Generation 1.5 BESS
  7 Energy Storage plants across Germany
    Starting capacity 11MWh
    Average 23.7MWh capacity
    Up to 67MWh capacity
    Sum of 187.6MWh
  Using mainly Samsung NMC Batteries
Main Usage cases:
  Primary Frequency Control (Main Usage scenario)
  Reduction of Distribution Grid Fees

## Slide 16: SMAREG4 – „Wartburgspeicher“
Customer | Investor project
Location | Eisenach
Completion | 2022
Power | 60 MW
Capacity | 60 MWh
System | SAMSUNG SDI
Design | 20x“Langhaus“ Design Rectifier Transformer
EMS | Smart Power iEMS
Technical Design
Key Facts

## Slide 17: SMAREG6 – „Gunzenhausen“
Customer | Investor project
Location | Gunzenhausen
Completion | 2023
Power | 24 MW
Capacity | 24 MWh
System | SAMSUNG SDI
Design | 2x Tripple „Langhaus“ Design Rectifier Transformer
EMS | Smart Power iEMS
Technical Design
Key Facts

## Slide 18: Agenda – Technical Portion
04
Overview – Historical Situation
The infrastructure which already existed
05
InfluxDB Cloud V1
Our journey to InfluxDB Cloud V1
06
InfluxDB Cloud Dedicated
Off to a shiny new cluster!
07
Gathering data with Telegraf from MQTT devices
How to harvest data from temporary sensor installations
08
Gathering data with Telegraf from Modbus devices
Gathering all information natively with Telegraf

## Slide 19: Overview – Historical Setup
04

## Slide 20: The Good Ol' Days
Centralised Monitoring Server:
  Rented vServer as the main influxDB Cluster
  No working backup solution
  Limitation of resources
  No upgrade of hardware/performance possible (dead end)
  Ubuntu Server installations close to end of life
Limitations of the legacy solution
  Unreliable syncing of data between Edge locations and centralised monitoring
  Due to Storage concerns, usage of retention policies to throw data out
  Due to throwing out data, analysis of the data is based on less precise information

## Slide 21: Limitations of the used InfluxDB OSS 1.x
Features which were introduced with later influxDB OSS Versions
  Edge Data Replication: reliable way to sync data from Edge locations
  Flux Language: More flexible and powerful queries
  Integrated UI: Built-in dashboarding and alert management
  Tasks: Automated data processing without Kapacitor
  Token-based Auth: Enhanced security and access control
  Export/Import: Easier backup and restore options

## Slide 22: InfluxDB Cloud V1
05

## Slide 23: InfluxDB Cloud V1 – The begin of the journey
Requirements
  More reliable server setup (simple failover functionality at least!)
  Implementation of snapshots and backups
  Prevention to delete data due to storage issues
  Getting a more reliable data sync into the cloud
  Migrate all existing data from self-hosted influxDB instances into Cloud instance
Solution
  InfluxDB Cloud V1 Cluster – multiple node setup
  Implementation of Kapacitor Tasks to send data through Kapacitor to the influxDB Cloud
  Getting rid of storage issues or concerns

## Slide 24: The problems and bottlenecks
Data Migration Headaches
  Due to the nature of our legacy infrastructure, using the influxDB OSS 2.x tools was not an option
  Importing the compressed line protocol exports took forever and failed a lot of times
Getting data into the Cloud
  Kapacitor tasks are running like a cronjob – no “real time” data ingests
  Kapacitor is not sending data multiple times if it failed the first time
Cluster load always spikes
  Cluster is having a hard time to keep up with the workload
  Even though not all legacy plants are ingesting data

## Slide 25: The problems and bottlenecks

## Slide 26: InfluxDB Cloud Dedicated
06

## Slide 27: The problems and bottlenecks
Data Migration Headaches
  Normalization of inconsistent data since InfluxDB V3 doesn’t support different data types per field
  Getting rid of legacy “retention” policies since storage isn’t a concern anymore
Getting data into the Cloud
  Using influxDB V2 write commands to send databases directly
  Running “inconsistent” databases through Telegraf to normalize the data
  Implementation of EDR for legacy plants
Cluster load
  Cluster is not having a hard time to keep up with the workload anymore
  All legacy plants are ingesting data now

## Slide 28: Introduction of EDR to Gen 1.0 Plants
Requirements
  More reliable transport from edge device data into cloud
  Avoiding to touch the actual plant control units, since touching the legacy scripts or SPS controls directly has a high risk potential of downtimes and interruptions
  Continuously data sending rather than getting data every 10mins
  Reliable mechanism to send back failed data
Solution
  Docker Compose “Swiss Army Knife” Container Setup which allows parallel installation to current local influxDB OSS
  Telegraf plays an influxDB v1 Listener
  Transfers data into influxDB OSS 2.4 Container
  Using EDR from the new influxDB Database
  Allows to keep all legacy scripts in place and no need to touch SPS
  Old Monitoring Server still gets data until all customers are migrated to the new Grafana instance

## Slide 29: Gathering data with Telegraf from MQTT devices
07

## Slide 30: Temporary temperature logging
Requirements
  During construction time, final climate incl. all sensors are not yet working
  We need to have logging information about the temperatures and humidity for batteries
  Due to this being just temporary, the systems need to be implemented quickly with low costs
Solution
  LAN Temperature Sensors which report data via MQTT
  Gathering the data from MQTT with Telegraf
  Sending the Telegraf data to local influxDB OSS
  Using EDR to send to InfluxDB Cloud Dedicated V3
  Add the database in Grafana for visualization and alerts

## Slide 31: Telegraf.conf file for getting the job done
Telegraf Setup
  Define MQTT Consumer Input Plugin
  Define InfluxDB V2 Output Plugin
  Configure MQTT input plugin
MQTT Input Plugin
  Set processing data format, i.e. ”xpath_json”
  Define the Metrics name and selection
  Define your field names and values

## Slide 32: Grafana Visualization of temporary temperature logging
Grafana Visualization
  Showing information about each device and sensor
  Adding the information to Dashboards
  Allows historical information checking
Grafana Alerts
  Since plants in construction phase, are not actively in monitoring like “production plants” the alerts are important to notify about temperature/humidity issues
Notes: Dashboard Link: https://grafana.juniz.energy/d/df2cf4a0-a527-45ab-b0ef-1dd670f7f95a/smareg9-temporare-temperaturueberwachung-baustelle?orgId=1

## Slide 33: Gathering data with Telegraf from Modbus devices
08

## Slide 34: Architecture Overview
Local Plant setup
  Each plant has local servers running influxDB OSS infrastructure
  Implementation of Telegraf to read Modbus data from devices directly
  Telegraf ”no code” solution allows agile development and deployments
  InfluxDB EDR takes care of reliable sending of data to the cloud

## Slide 35: InfluxDB Solution Partner – B1-Systems
About B1-Systems
  B1 Systems is a worldwide operating provider of Consulting, Training, Managed Service & Support around Linux/Open Source with more than 150 employees
  Areas of expertise
  Container and Virtualization
  Public & Private Cloud
  High Availability Cluster
  Configuration & System Management
  Monitoring & Log Management
  Products
  Client, Display & Server Management
  Locations
  Rockolding
  Cologne
  Berlin
  Dresden
  Jena
Notes: Dashboard Link: https://grafana.juniz.energy/d/df2cf4a0-a527-45ab-b0ef-1dd670f7f95a/smareg9-temporare-temperaturueberwachung-baustelle?orgId=1

## Slide 36: Telegraf.conf file for getting the job done
Telegraf Setup
  Define Modbus Input Plugins
  Define Modbus registers for each sector of the plant
  Configure InfluxDB Output Plugin
  Configure – depending on plant size – multiple telegraf.conf files to allow parallel data querying
  “No Code” solution without dependencies for modifications unlike SPS

## Slide 37: Grafana Visualization of BESS
Grafana Visualization
  Adding variables which allows flexible investigation of data
  No performance issues – if you check one battery or twenty
  Dashboards can be used for automated reporting
  Standardized dashboards allow quicker deployments and connecting new projects into the monitoring
Notes: Dashboard Link: https://grafana.juniz.energy/d/df2cf4a0-a527-45ab-b0ef-1dd670f7f95a/smareg9-temporare-temperaturueberwachung-baustelle?orgId=1

## Slide 38: Improving the Alert mechanism for both Generation BESS Systems
Grafana Multi-Dimensional Alerts
  Allows complex alert conditions based on multiple metrics
  Supports time-based conditions (e.g., alert if SOC < 20 for 15 mins)
  Provides greater context, reducing false positives
Sending Grafana Alerts Through Opsgenie
  Direct Integration of Grafana Alerts with Jira Ticket System
  Allows on-call scheduling and routing rules
  Allows additional notification in case of emergency, i.e. via SMS and phone call
  Creating Jira Tickets via Opsgenie
  Auto-generate Jira tickets for specific alert conditions
  Streamlines incident management workflow
Notes: Dashboard Link: https://grafana.juniz.energy/d/df2cf4a0-a527-45ab-b0ef-1dd670f7f95a/smareg9-temporare-temperaturueberwachung-baustelle?orgId=1

## Slide 39: Grafana Alerts
Notes: Dashboard Link: https://grafana.juniz.energy/d/df2cf4a0-a527-45ab-b0ef-1dd670f7f95a/smareg9-temporare-temperaturueberwachung-baustelle?orgId=1

## Slide 40: Grafana Visualization of BESS
Grafana Visualization
  LIVE DEMONSTRATION – SWITCH TO BROWSER AND CONTINUE HERE LATER
Notes: Dashboard Link: https://grafana.juniz.energy/d/df2cf4a0-a527-45ab-b0ef-1dd670f7f95a/smareg9-temporare-temperaturueberwachung-baustelle?orgId=1

## Slide 41: Summary and next projects/steps
Getting Data with Telegraf
  Telegraf supports wide range of devices and communication protocols
  Allows easy integration – like influxDB Database – “no need to think about it twice”
  Supported and integrated in a wide range of products, i.e. our firewalls have a Telegraf plugin
InfluxDB Edge Data Replication
  Makes sending data stable even with unreliable network connections
  Reliable re-sending of failed metrics
  InfluxDB Cloud Dedicated
  (Nearly) no need to think about storage costs and usage anymore
  Way better compression compared to influxDB Cloud V1 or OSS
  Next projects and steps
  Evaluating communication between our SPS controllers and Telegraf with OPA-UA
  Evaluating communication between our SPS controllers and Telegraf with MQTT
  Integration of EPEX SPOT data
  Centralised cluster for analytics between batteries and market data
Notes: Dashboard Link: https://grafana.juniz.energy/d/df2cf4a0-a527-45ab-b0ef-1dd670f7f95a/smareg9-temporare-temperaturueberwachung-baustelle?orgId=1

## Slide 42: energy transition
We take responsibility for our actions, ask questions, even the uncomfortable ones, and courageously try out new approaches.
Where you can
get
involved
We're hiring like crazy – not limited to IT jobs! Find out about your next big move at ju:niz. 🚀
Wanna shape the
www.juniz.com
Interested in pushing our shiny new InfluxDB Cloud Cluster to the max? Let's sit down for a coffee and discuss your path to joining the ju:niz team.😁